HP48SX Modeming
 
 
In general, one can keep a modem well-fed and happy by connecting
pin 6 (data set ready) to pins 4 (ready to send) and 20 (data terminal
ready).  When the modem is on, it should assert DSR, but it may wait
for RTS or DTR to be asserted before doing anything else.
 
Upon satisfying pins 4 and 20, connecting pins 2, 3, and 7 to the
calculator will suffice to use the modem.  To avoid (or create)
confusion, I will letter the pins on the calculator as A, B, C, and D,
starting with the pin closest to the IR led/detector pair.  Then
connect A to 7, B to 3, and C to 2 (and if you want, connect D to
the cable shield, if any).  The pin 2 and 3 connections are opposite
what you would use to connect to a computer, since computer serial
ports are wired like terminals ("data terminals"), not modems ("data
sets").
 
Mark Adler
madler@tybalt.caltech.edu