*****************************AUTOEXEC.NET**************************************
#
# General setup.  Note that all IP addresses and domain names are fictitious.
#
scrollback 0
isat on
hostname myhost.domain.name
#
# Set up ethernet link
#
attach packet 0x60 en0 20 1500
ifconfig en0 ipaddr 192.0.2.1
ifconfig en0 netmask 0xffffff00
ifconfig en0 broadcast 192.0.2.255
arp add 192.0.2.255 ethernet ff:ff:ff:ff:ff:ff
#
# Set up autodial Van Jacobsen compressed SLIP link @ 57.6K bps
# with RTS-CTS flow control.
#
#attach asy 0x3f8 4 vjslip sl0 4096 1500 57600 cr
#ifconfig sl0 ipaddr 1.0.0.1
#ifconfig sl0 netmask 0xffffff00
#ifconfig sl0 broadcast 1.0.0.255
#
# Broadcast default route with RIP every 30 seconds
#
route add default sl0 1.0.0.2 1
start rip
rip add 192.0.2.255 30 1
#
# Configure name lookup
#
domain suffix domain.name
domain addserver 192.0.2.2
#
# Start daemons.
#
start ftp
remote -s ratinthevat
start remote
#
# Start packet logging.
#
ip log 192.0.2.2:514
#
# Set up packet filter on SLIP link.
#
ip filter sl0 permit in tcpxsyn !192.0.2.0/24     192.0.2.0/24
ip filter sl0 permit in icmpxrd !192.0.2.0/24     192.0.2.0/24
ip filter sl0 permit in udp     !192.0.2.0/24:53  192.0.2.0/24:53
ip filter sl0 permit in udp     !192.0.2.0/24:53  192.0.2.0/24:1024+
ip filter sl0 permit in udp     !192.0.2.0/24:123 192.0.2.0/24:123
ip filter sl0 permit in tcpsyn  !192.0.2.0/24:20  192.0.2.0/24:1024+
ip filter sl0 permit in tcpsyn  !192.0.2.0/24     192.0.2.0/24:25
ip filter sl0 permit in tcpsyn  !192.0.2.0/24     192.0.2.2:79
ip filter sl0 log deny in *     *                 *
ip filter sl0 permit out *      192.0.2.0/24      !192.0.2.0/24
#
# Enable dialer.  Do this last so filtering will be up before the link.
#
dialer sl0 1000 SLIPDIAL SLIPDOWN SLIPDOWN
*******************************************************************************

AUTOEXEC.NET is the KA9Q initialization file read at startup.


*********************************SLIPDIAL**************************************
speed 57600
control up
wait 500
send "ATDTW 555-1212\r"
wait 35000 "CONNECT"
wait 20000 "login: "
send "user69\r"
wait 5000 "Password: "
send "password105\r"
wait 5000 "Packet mode enabled"
*******************************************************************************

SLIPDIAL is the autodialer script executed when the link is down and
packets need to be routed.


*********************************SLIPDOWN**************************************
control down
wait 5000
control up
*******************************************************************************

SLIPDOWN is the script executed when the link has been idle for the
interval specified in the dialer command.


*********************************FTPUSERS**************************************
mischler siegelgrund / 127
*******************************************************************************