## Slide 1: XT# Hardware Architecture
John M. Levesque
Director
Cray Supercomputing Center of Excellence
CSC, Finland
September 21-24, 2009

## Slide 2: An overview of Cray XT systems
 | XT3 | XT4 | XT5 | XT6
Number of cores/socket | 2 | 4 | 4-6 | 12
Number of cores/node | 2 | 4 | 8-12 | 24
Clock Cycle (CC) | 2.6 | 2.3 | 2.6 | ??
Number of 64 bit Results/CC | 2 | 4 | 4 | 4
GFLOPS/Node | 10.4 | 36.8 | 83.6-124.8 | ~200
Interconnect | Seastar 1 | Seastar 2+ | Seastar 2+ | Gemini
Link Bandwidth GB/sec | 6x2.4 | 6x4.8 | 6x4.8 | 10x4.7
MPI Latency microseconds | 6 | 6 | 6 | 1.5
Messages/sec | 400K | 400K | 400K | 10M
Global Addressing | No | No | No | Yes

## Slide 3: Cray XT4 Node
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
2 – 8 GB
12.8 GB/sec direct connect memory (DDR 800)
6.4 GB/sec direct connect HyperTransport
Cray SeaStar2+ Interconnect
4-way SMP
>35 Gflops per node
Up to 8 GB per node
OpenMP Support within socket
Notes: Point out 800 Mhz memory (new)

## Slide 4: Cray XT5 Node
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
9.6 GB/sec
2 – 32 GB memory
6.4 GB/sec direct connect HyperTransport
Cray SeaStar2+ Interconnect
25.6 GB/sec direct connect memory
8-way SMP
>70 Gflops per node
Up to 32 GB of shared memory per node
OpenMP Support

## Slide 5: XT Hardware Socket
Budapest | Barcelona | Shanghai | Istanbul
4 FPS/CC | 4 FPS/CC | 4 FPS/CC | 4 FPS/CC
64KB | 64KB | 64KB | 64KB
512KB | 512KB | 512KB | 512KB
2048KB | 2048KB | 6144KB | 6144KB
Core
Core
Core
Core
L1
L2
L2
L2
L2
Level 3 Cache
L1
L1
L1

## Slide 6: Simplified memory hierachy on the Quad Core AMD Opteron – Quad Core
…...
registers
L1 data cache
L2 cache
16 SSE2 128-bit registers
16 64 bit registers
2 x 16 Bytes per clock loads or 1 x 16 Bytes per clock store, (76.8 GB/s or 38.4 GB/s on 2.4 Ghz)
Main memory
64 Byte cache line
complete data cache lines are loaded from main memory, if not in L2 or L3 cache
if L1 data cache needs to be refilled, then storing back to L2 cache, if L2 needs to be refilled, storing back to L3
Items in L1 and L2 are exclusive, L3 is “sharing aware”
write back cache: data offloaded from L1 data
cache are stored here first
until they are flushed out to main memory
Pre-fetching can go to L1 or L2 cache
16 Bytes wide => 12.8 GB/s for DDR2-800, 73ns
16 Bytes per clock,
38.4 GB/s BW
…...
Shared L3 cache
32 GB/s
Remote memory
8GB/s over coherent Hyper Transport, 115ns

## Slide 7: XT Hardware Node
Core
Core
Core
Core
L1
L2
L2
L2
L2
Level 3 Cache
Memory
Memory
2 HT Links
1 HT Links
Interconnect
L1
L1
L1
Core
Core
Core
Core
L1
L2
L2
L2
L2
Level 3 Cache
L1
L1
L1
12.8 GB/sec
12.8 GB/sec
6.4 GB/sec
12.8 GB/sec
115 ns
8 GB/sec
73 ns
73 ns

## Slide 8: What are the strengths and bottlenecks of the hardware
Strengths
  Upgradability
  Scalability of interconnects
  Increased node performance – need to use fewer nodes to achieve same performance
  Global addressing with Gemini
    Adds ability to use PGAS – UPC And CAF to program around some of the weaknesses

## Slide 9: What are the strengths and bottlenecks of the hardware
Bottlenecks
  Memory bandwidth will never be enough to support all the cores
    Need to think about programming around this
      PGAS – UPC and CAF
      OpenMP
  Injection Bandwidth will never be enough to support all the cores
    Need to think about programming around this
      PGAS – UPC and CAF
      OpenMP
  Global Bandwidth will never be enough to support ALL to ALLs across all of the cores
    Need to think about programming around this
      PGAS – UPC and CAF
      OpenMP

## Slide 10: Common message
Need to investigate Hybrid programming
Need to investigate use of PGAS
  Global Arrays
  UPC
  Co-Array Fortran
  SHMEM