ES1:  This is a partial picture of my control "board".

Lower left is two variacs which I run in series to control the speed of the
rotary gap motor.  One is set to limit the maximum rpm and the other is used
to bring the speed up slowly.  Above these are the 60 cycle supple lines
going out to the coil.  One is for the rotary gap motor, the other is for the
fan motors on the rotary and the static gap used in series.

The heavy powerstat variac is in the center bottom - used to contro the
voltage to the pole pig.  Above that is the ammeter and voltmeter to monitor
the pole pig primary.  Above that you can see the primary feed lines going to
the pole pig.

To the right, are the 60 cycle line filters and some home made toroid filters
used in series with the 60 cylce ground connection.

Upper right is the plug for the welder (used to limit pole pig primary
current) and the plug for the resistive bank (oven elements) used in parallel
with the welder primary also to control the pole pig primary current.