SPARKGP1 GIF and SPARKGP2 GIF  (1024x768 and 800x600)

 These are two scans of a spark gap system that I designed and
 built for operation at power levels between 1 - 5 kVA. This
 particular gap system has been very successful and has seen
 many hours of run time. The quench time is low enough that
 small Tesla Magnifiers can be fired without problem despite
 the very close coupling factor between the primary and secondary
 coils in Magnifier systems.

 The small rotary gap in the center has eight tungsten electrodes
 mounted on a steel ring. The ring is bolted to a multi-layer
 marine grade fiberglas board that insulates the conductive ring
 from the motor shaft. The motor is a Bodine 1/10 horse-power
 fixed speed that rotates at 3450 rpm. The two stationary elect-
 rodes are also tungsten, mounted on high temperature porcelain
 insulators with heavy brass caps. The motor and stationary
 electrodes are mounted to a custom made base of butchers block.
 This particular rotary gap was designed and built by Gary Legel
 of California, and I was lucky enough obtain it when he was
 scaling back on his coiling equipment. It had obviously never
 used when I unpacked it!

 In series with the rotary gap, one on either side, are two
 custom cylinder static gaps. These two cylinder static gaps
 do most of the quenching, leaving the rotary gap to simply
 commutate the arc.

 This photo is taken from above. The gap system is sitting on the
 gap shelf on my rolling Tesla coil workstation. Barely visible
 below the gaps are the sides of three capacitors stored in the
 workstation.

  System was designed, built, and operated by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA; with
 the exception of the custom rotary gap which was designed and
 constructed by Gary Legel, 1306 Sheppard Dr., Fullerton, CA
 92631  USA