PICE1024.GIF and PICE800.GIF

 These are scans (1024x768 & 800x600) of Richard Hull's old coil
 "Nemesis" producing 10 - 12 foot arcs across his lab. Nemesis is
 now dismantled and has been replaced with more efficient Tesla
 Magnifier systems. The secondary coil was wound on a sealed thin
 wall PVC flume duct fourteen inches in diameter, with a winding
 forty-two inches long of No. 18 AWG double Formvar magnet wire.
 The secondary had just over 1000 turns and resonated bare at
 about 100 kHz. Loaded with the very large toriod discharger this
 system resonated around 50 - 60 kHz.

 The tank circuit capacitance was only .09 microfarads. The low
 tank circuit frequency required to match this secondary is
 ahieved with a large 14 turn saucer shaped primary coil tapped
 out at over 12 turns. The power supply is a custom wound pole
 pig ballasted with both inductance and resistive elements, with
 the actual power delivered to the tank circuit at about 10 kVA.
 The spark gap system uses a medium sized rotary spark gap with
 a vacuum quenching static gap in series. The toriod discharger
 is homemade from commercial ventilation ducting and has pro-
 tuberances deliberatly added to disrupt the field and force the
 spark discharge towards the camera.

 Note the electronic test and diagnostic equipment being brutally
 struck by the discharges: Richard Hull is no fool, modern solid
 state equipment would be junk after this treatment, Richard has
 purchased old tube equipment for pennies on the dollar to outfit
 his lab. Only tube equipment could withstand this abuse.