From rwstephens@ptbo.igs.net Wed Apr 24 19:55:58 1996

mtc01rws.jpg
This is me standing in my test room with my newly built medium sized 
Tesla coil (November'95)shown here with 8 inch by 30 inch toroid.  
Secondary is #18 AWG, PVC insulated wire, closewound to a length of 
4 feet on a 15 inch diameter, 1/2 inch wall  PVC form. Unit operates 
at about 100KHz.  Rotary break at 400 PPS.  Present maximum power 
capability 4.6 kVA (20 amps@230 volts) was used in this photo group.  
Has produced up to 9 foot streamers at this power level. This unit is 
a production prototype demonstrator from my line of custom built Tesla 
coils available for sale.

mtc02rws.jpg
Medium TC in unusual neat shot of single horizontal streamers under full room 
lighting.

mtc03rws.jpg
Medium TC with larger 10 inch by 35 inch topload being tested.  7.5 foot 
streamers to overhead  grounded strike wires.

mtc04rws.jpg
Medium TC. Six foot streamers to right strike curtain.

mtc05rws.jpg
Medium TC.  8.2 foot streamer to strike curtain in upper right.

mtc07rws.jpg
First outdoor test of my medium T.C. at increased input power of 6.9
kVA(30A @ 230V), and with new, larger 12" x  48" toroid.  A measured
twelve foot point-to-point streamer darts off  frame to the left to 
connect with the tin roof of my shop.

mtc08rws.jpg
First outdoor test of my medium T.C. at increased input power of 6.9 
kVA (30A @ 230V), and with new, larger 12"x 48" toroid. Many strikes 
to protective ground wire and one to the primary strike ring.

mtc09rws.jpg
First outdoor test of my medium T.C. at increased power of 6.9
kVA (30A @ 230V), and with new, larger 12"x 48" toroid.  Destructive 
testing of a wooden ladder and 4 foot fluorescent lamp in progress.

mtc11rws.jpg
First outdoor test of my medium T.C. at increased power of 6.9
kVA (30A @ 230V), and with new, larger 12"x 48" toroid.  This photo 
proves that you don't have to "connect" to a fluorescent lamp to 
illuminate it.

mtc12rws.jpg
This is my hand.  This is my hand on my medium T.C.  Any questions?